## Slide 1: Automated Segmentation of 3D Electron Microscopy Images
Joris Roels
Notes: Thank you Mr. Chairman for the kind introduction. Dear members of the examination board, dear colleagues, friends and family. I would like to welcome you and thank you for coming.

## Slide 2
2.09 million
1.76 million

## Slide 3: Lung cells under the microscope
Healthy cells
Cancer cells

## Slide 4: Potential cause for lung cancer
Mitochondria: energy generators
Endoplasmic reticulum (ER): transportation network
Cells receive too much energy
Cells become bigger
Number of cells increases

## Slide 5: Life science research
Growing interest in analysis mitochondria & ER:
Alzheimer’s disease
Parkinson’s disease
Dementia
Cancer
…

## Slide 6: Problem statement
Visualisation of mitochondria & ER is difficult
Light microscopy
Electron microscopy
Noise
Blur

## Slide 7: Problem statement
Quantitative analysis of mitochondria & ER is even more difficult
Measure total ER volume?
How many contact points with mitochondria?
…

## Slide 8: Outline
Introduction to 3D electron microscopy (EM)
Image restoration in 3D EM
  Noise & blur analysis
  NLM-SC
  PV-DEC
  Image restoration in practice: DenoisEM
Image segmentation in 3D EM
  Ensemble networks
  Towards less expert intervention: weak annotations
  Segmentation of new data: domain adaptation
Conclusion

## Slide 9: Introduction to 3D electron microscopy

## Slide 10: The need for high resolution imaging
Mitochondria
(0.5 – 10 m)
ER sheets
(10 – 50 nm)

## Slide 11: 3D EM imaging
2D imaging with an electron beam
Sectioning with a diamond knife

## Slide 12: 3D EM data
HeLa cell

## Slide 13: Degradations in EM imaging
Noise
Blur

## Slide 14: Outline
Introduction to 3D electron microscopy (EM)
Image restoration in 3D EM
  Noise & blur analysis
  NLM-SC
  PV-DEC
  Image restoration in practice: DenoisEM
Image segmentation in 3D EM
  Ensemble networks
  Towards less expert intervention: weak annotations
  Segmentation of new data: domain adaptation
Conclusion

## Slide 15: Image restoration in 3D EM

## Slide 16: EM image restoration: how it is currently done
Gaussian filter:
 Average pixels locally to denoise the reference pixel
Acquired image
Restored image
Blur introduction along edges

## Slide 17: Non-local means (NLM)
For each pixel:
  Find (non-local) similar regions
  Compute weights for each region:
    Similar region  high weight
    Dissimilar region  low weight
  Restore pixel by weighted averaging
0.05
0.35
0.60

## Slide 18: NLM: results
Degraded image
NLM

## Slide 19: Noise estimation
Switch off the electron beam (“take a picture in a dark room”)
 Noise signal
Noise correlation model

## Slide 20: Proposed method: NLM-SC
Noise prewhitening: undo the correlation
Compute weights on the prewhitened image
0.10
0.30
0.70
Inversion
Noise correlation model

## Slide 21: Proposed method: NLM-SC
Prewhitening improves window comparison
Degradation-free
Prewhitening
No prewhitening

## Slide 22: Results
Chart: 
| 2.5000000000000001E-2 | 0.05 | 7.4999999999999997E-2 | 0.1 | 0.125
Gaussian filter | 25.66 | 24.58 | 23.85 | 23.29 | 22.83
NLM | 25.72 | 24.56 | 23.77 | 23.18 | 22.7
NLM-SC (proposed) | 25.98 | 25.02 | 24.15 | 23.49 | 22.86
PSNR
(dB, higher is better)
Noise level

## Slide 23: Results
Ground truth
Degraded image
NLM
NLM-SC (proposed)
Gaussian filter

## Slide 24: Blur estimation
Acquire binary samples that should have crisp edges
1D edge extraction

## Slide 25: Blur estimation
Inversion
Estimate a 1D kernel from the measured edge signals
Measured kernel
Fitted kernel
Averaging
Measured signal
True signal
Radial symmetry

## Slide 26: Primal-variational deconvolution (PV-DEC)
Model the complete physical pipeline statistically:
Blur introduction ()
Poisson noise introduction ()
Gaussian noise introduction ()
Imperfect magnetic lenses, focusing
Sensor counting errors
Electromagnetical interference
Original image
Acquired image

## Slide 27: Primal-variational deconvolution (PV-DEC)
Model the complete physical pipeline statistically:
Introduce the image without Gaussian noise:
What pair would make , and the most likely acquired image?

## Slide 28: Primal-variational deconvolution (PV-DEC)
Does this image have a Gaussian distribution?
Does this image have a Poisson distribution?
How likely is this image?
Model the complete physical pipeline statistically:
Introduce the image without Gaussian noise:
What pair would make , and the most likely acquired image?

## Slide 29: Sparsity as a prior
Transform the image to an alternative representation that should be sparse
Wavelet transform
Inverse wavelet transform

## Slide 30: Results
Chart: 
| 2.5000000000000001E-2 | 0.05 | 7.4999999999999997E-2 | 0.1 | 0.125
Gaussian filter | 25.66 | 24.58 | 23.85 | 23.29 | 22.83
NLM | 25.72 | 24.56 | 23.77 | 23.18 | 22.7
NLM-SC | 25.98 | 25.02 | 24.15 | 23.49 | 22.86
PV-DEC | 27.46 | 25.98 | 24.66 | 23.82 | 23.45
PSNR
(dB, higher is better)
Noise level

## Slide 31: Results
Ground truth
Degraded image
NLM-SC
PV-DEC (proposed)
Gaussian filter

## Slide 32: The importance of parameters
How do we tune parameters to optimality as fast as possible?

## Slide 33: DenoisEM: introducing the human in the loop
GPU accelerated backend

## Slide 34: DenoisEM

## Slide 35: Outline
Introduction to 3D electron microscopy (EM)
Image restoration in 3D EM
  Noise & blur analysis
  NLM-SC
  PV-DEC
  Image restoration in practice: DenoisEM
Image segmentation in 3D EM
  Ensemble networks
  Towards less expert intervention: weak annotations
  Segmentation of new data: domain adaptation
Conclusion

## Slide 36: EM Image Segmentation

## Slide 37: EM image segmentation: how it is currently done
Manual labeling
 Time consuming
mm3
Reconstruction of all neurons required 4 years using 224 grad students

## Slide 38: EM image segmentation: how it is currently done
Automated techniques
 Insufficient quality
Input
Automatically generated segmentation with current techniques
Ground truth

## Slide 39: Classical image segmentation techniques
Extract hand-designed features from data
  Intensity
  Edges
  Texture
  Shape
Learn to combine these features to obtain the segmentation based on a set op labeled examples
Which features?

## Slide 40: Advanced image segmentation: convolutional neural networks (CNNs)
Compute the segmentation by computing features layer by layer with basic operations (convolution, truncating, maximum, …)

## Slide 41: Advanced image segmentation: convolutional neural networks (CNNs)

## Slide 42: Advanced image segmentation convolutional neural networks (CNNs)
Feature extraction is “trained” iteratively by looking at labeled examples
Compute segmentation
Optimise parameters
Parameters layer 1
Parameters layer 2
Parameters layer 3

## Slide 43: State-of-the-art architectures
Classical CNN
FCN
U-Net

## Slide 44: CNN-based segmentation: results
Quality measure:
 | Mitochondria | ER
CNN | 0.752 | 0.309
FCN | 0.871 | 0.594
2D U-Net | 0.877 | 0.614
3D U-Net | 0.890 | 0.635
Jaccard =
Intersection(S,GT)
Union(S,GT)
0.24
0.89

## Slide 45: CNN-based segmentation: disadvantages
3D labels are hard to obtain, 2D labels are easier
Too much labeled data required
Networks do not generalise well to new data
Scanning EM
Transmission EM

## Slide 46: An ensemble of 2D networks

## Slide 47: Results: 2D ensembles
Jaccard | Training time | Testing time
87.74 | 6h 1m 4s | 39s
88.99 | 2d 7h 8m | 5m 13s
88.62 | 8h 14m 39s | 2m 1s
Segmentation & computational performance:
Input + ground truth
U-Net (2D)
U-Net (3D)
Ensemble

## Slide 48
Mitochondria segmentation result for 2D ensemble

## Slide 49: CNN-based segmentation: disadvantages
3D labels are hard to obtain, 2D labels are easier
Too much labeled data required
Networks do not generalise well to new data
Scanning EM
Transmission EM

## Slide 50: Towards less supervision: weak labels
Strong supervision:
High labour intensity
20 seconds / image
Weak supervision:
Low labour intensity
2 seconds / image (image-level)
2 seconds / image (point-level)
4 seconds / image (squiggle-level)
Pixel-level
Image-level
Point-level
Squiggle-level

## Slide 51: Object localisation with weak labels
Activation in CNN trained on weak mitochondria labels
Activation in CNN trained on weak ER labels

## Slide 52: Weakly supervised pretraining
Pretrain the encoder with lots of weak labels (cheap)
Finetune the complete network with few strong labels (expensive)

## Slide 53: Weakly supervised pretraining: results
Weak labels:
  0, 512, 2048 annotated images
  2 seconds / image
Strong labels
  10, …, 100 annotated images
  20 seconds / image

## Slide 54: CNN-based segmentation: disadvantages
3D labels are hard to obtain, 2D labels are easier
Too much labeled data required
Networks do not generalise well to new data
Scanning EM
Transmission EM

## Slide 55: What about new datasets?
Data
Reconstruction
High-level analysis:
Counting
Volume measuring
Shape modeling
…
Image segmentation
?
?
?

## Slide 56: Domain adaptation: learning from other labels
Target data
Source data
Source labels
Predictive model
Target prediction

## Slide 57: Y-Net: reconstruction-based domain adaptive segmentation
Add a reconstruction decoder for source and target
Feature encoder finds features for source/target reconstruction and source segmentation
Feature encoder
Segmentation decoder
Reconstruction decoder

## Slide 58: Y-Net: results
 | No DA | Y-Net
Jaccard | 28.70 | 49.55
Ground truth
No adaptation
Y-Net
Scanning EM
Transmission EM

## Slide 59
DA segmentation for the reconstruction of ER

## Slide 60: Conclusion
Novel image restoration techniques: recover detailed structures in 3D EM data
DenoisEM: denoising plugin accessible to the life science community
New segmentation algorithms: less manual intervention & better performance
Domain adaptive segmentation: better performance on new datasets
International collaboration

## Slide 61: Thank you!